## Slide 1: Compiler Management of Communication and Parallelism for Quantum Computation
Authors: Jeff Heckey, Shruti Patil, Ali Javadi Abhari, Adam Holmes, Daniel Kudrow, Kenneth R. Brown, Diana Franklin, Frederic T. Chong, Margaret Martonosi (ASPLOS ‘15)
Slides by: George Li

## Slide 2: Objective
Proposes a muti-SIMD (single instruction, multiple datastream) scalable quantum computing architecture, using microwave control fanout, quantum teleportation and global/local memories
  Efficient use of Multi-SIMD requires orchestration of qubits to maximize parallelism and to reduce qubit move/teleport operations, so communication-aware scheduling techniques are the main focus

## Slide 3: Ion Trap Technology
Trapped-ion systems seem the most promising candidate for large scale QC (2015)
  Well characterized qubits; long decoherence; can initialize, measure, and perform universal set of gates
Laser tuning for phase must be extremely precise, limiting QCs to ~6-12 lasers because they’re too big
Experiments with microwaves show potential multi-qubit control scalability from 10-100 qubits for a single microwave emitter; additional fanout level could create SIMD regions for ~100-10,000 qubits
  Microwave control doesn’t actually allow for measurement, so assume laser-controlled measurement

## Slide 4: Quantum Teleportation
EPR (Einstein-Podolsky-Rosen) pair q2/q3 pre-distributed between communication regions before teleportation, q3 is used as destination
States q1 and q2 are measured, then classically transmitted to q3 via X and Z operations
  q1 state destroyed in process
Teleportation process requires up to 4x the communication cost of a single qubit
  Assume all gates with same latency
  Scheduling algorithm should optimize to minimize QT operations
  Allows for simplified global memory to make long distance communication constant

## Slide 5: Multi-SIMD Architecture Model
k SIMD compute regions with d qubits each
  k limited by number of microwave signals, d limited by fanout without disturbing system
Uses microwaves to control states
Each region has a teleportation unit and local memory, as well as a global memory for scheduling purposes
QT uses classical communication channels, which reduces quantum decoherence over repeatedly moving qubits on physical fabric

## Slide 6: Multi-SIMD Architecture (cont.)
The k SIMD regions can be used as active computation as well as passive storage for qubits
Active qubits must be moved between regions, idle qubits moved to global memory
  Using local memory could reduce overhead
  Centralized global memory model assumes QT latency constant
  Constant cost favors parallelism; memory access takes same time for serial vs parallel
    With simplified model, local memory assumed to take 1 compute cycle, global memory takes 4

## Slide 7: Compiler Framework
Uses ScaffCC for scheduler
  Translates algorithms in Scaffold into LLVM, then into QASM
  for loops and state-based conditional statements allows for parallelism control
  QASM uses qubits, cbits, and instruction set of universal gates (X, Y, Z), CNOT, H, Phase (S), and π/8 (T) gate
    QECC Sub-operations below logic level are not optimized
Classical-To-Quantum-Gates (CTQG) integrated into flow
  Decomposes arithmetic operations and if-then-else into QASM
Compiler uses decomposition stage to translate rotation and Toffoli gates into approximate equivalents
  Scheduling is targeted after this decomposition step
  Full unrolling using iteration counts, gate operations available w/ Scaffold; too large for benchmarks
  Extend LLVM intermediate of ScaffCC to also analyze modules for leaf and non-leaf hierarchies
    Allows for fine grained and coarse grained scheduling of leaf modules

## Slide 8: Leaf Module Flattening Example
Two dependent toffoli operations in example
  Toffoli operation decomposed into QASM gates
  Modular case (coarse grained) does not detect inter-blackbox parallelism

## Slide 9: Flattening Results
Flattening Threshold (FTh) – resource estimation on each module to count number of gates
If less than threshold it is “flattened”
  80% of modules were flattened

## Slide 10: Execution and Scheduling Model
Multi-SIMD(k,d) model allows 1 to k discrete, simultaneous gates to executed in one logical timestep, each which can be applied on 1 to d qubits each
  Gate operations assumed to take one logical timestep, constrained by longest operation time
Compiler assume modules are blackboxes, so all active qubits are flushed to global memory during calls
  Assume ancilla bits are generated by global memory and teleported to SIMD needed
  QT between SIMD regions must also be scheduled
    Schedulers need to account for data movement costs; QT uses 4 timesteps, which results in a potential 5x longer runtime than computed critical path
Schedules are a list of sequential timesteps, each timestep contains an array of k+1 SIMD regions
  0th region lists the qubits that will be moved and corresponding sources and destinations
  Rest list the operations to be performed in the associated region

## Slide 11: Scheduling with Ready Critical Path (RCP)
Method for scheduling tasks to prioritize those which take the longest, and schedule other tasks during this time to not delay the next dependency
  Identifies the longest chain of successive dependent activities and associated time to identify critical paths
  Schedule other tasks alongside this timing constraint to minimize delay
Maintains a ready list instead of a free list for tasks, and only queues tasks with dependencies met
  Unsorted list of operations
Evaluates operation type, movement cost, and slack
  Slack is graph distance between uses of a qubit
  Can also weight each of these, but set to 1 for this case
Visualization of critical path method
https://en.wikipedia.org/wiki/Critical_path_method#/media/File:SimpleAONwDrag3.png

## Slide 12: Ready Critical Path Algorithm
At each timestep, priority for each operation type in each SIMD is calculated with its associated region and operation
  When priority for configurations have been calculated, the SIMD region and operation type with highest priority is scheduled
    SIMD region is removed from available regions
    Ready list updated
  Repeat until all operations in ready list are scheduled or all regions occupied
  Then update ready list with operations ready for next timestep until queue is empty

## Slide 13: Longest Path First Search (LPFS)
LPFS assigns l SIMD regions, where l < k for l longest paths
Longest path algorithm starts by finding the critical path in the LLVM generated DAG (directed acyclic graph)
Illustration of linearization of DAG
http://www.mathcs.emory.edu/~cheung/Courses/171/Syllabus/11-Graph/Docs/longest-path-in-dag.pdf

## Slide 14: LPFS Algorithm
Start at the top, sets a tag at each node with the furthest distance from the top
  Find largest depth from bottom, then trace back and record paths
    Multiple paths can be found sequentially and at arbitrary positions in the execution
    Longest paths returned as ordered list of the operations to be performed
      Stored in array of size l for each statically scheduled region
  Operations not on any of the longest paths added to a free list
    Scheduled in any available SIMD in range [l+1, k] based on order of operations as they are scheduled
  2 more options SIMD & Refill
    SIMD scheduling allows any SIMD region dedicated to longest path to execute an operation from the free list of the same type
    Refill lets longest paths of unequal lengths to schedule another path to schedule after the first finished; refill a reserved SIMD with another longest path
    Experiments run with l = 1 and SIMD and Refill enabled

## Slide 15: Scheduling Algorithm
Because benchmarks are so large, coarse-grained scheduler stiches together the optimized leaf modules scheduled by RCP and LPFS
  Algorithm for k SIMD regions
  Operations are scheduled in priority order
  Flexible blackbox dimensions considered for parallelizable modules to find the best combination
For each operation Fi in priority ordered set
  Check dependencies for scheduling timestep
    If dependencies don’t allow for it, serialize Fi into own schedule
  Find l & w of operation
    If it fits into constraints, just add to schedule of current block
      If not, try different combinations of length and width to see if any will fit
        If so, add it to schedule of box
        If not, serialize operation into own box
  Merge current box with total box dimensions

## Slide 16: Scheduling Communication with Local Memory
To further reduce communication overheads, a rudimentary optimization using local memories attached to SIMD regions
  Computed after communication-aware algorithm has finished mapping computations to SIMD and communication schedules are computed
    Determine if some qubits can be moved to local memory instead of teleporting to global memory
      Based on when the qubit’s next computation is scheduled
        Local memory also constrained by capacity
    Qubit can be stored in global memory, source local memory, destination local memory, or an idle SIMD region
      Unless source SIMD region is idle, qubits moved to global memory
      After each compute cycle, qubits not scheduled for next operation are moved to global or scratchpad memory; reused ones are left in place
  Local moves are derived from the schedules on leaf modules and the schedule is modified to reflect moves.
    If any region requires a move to/from global memory, wait 4 cycles to avoid race condition

## Slide 17: Benchmarks Used
Benchmarks modularly describe quantum circuit acting on logical qubits. Range from 10^7 to 10^12 gates.
  Grover’s Search
    Amplitude amplification to search database of 2^n elements, parameterized by (n)
  Binary Welded Tree
    Uses random walk algorithm to find path between entry and exit node.
    Parameterized by height (n) and time (s) to find solution
  Ground State Estimation
    Quantum phase estimation algorithm to estimate ground state energy of molecule. Parameterized by size of molecule in terms of molecular weight (M)
  Triangle Finding Problem
    Finds a triangle in dense, undirected graph; parameterized by nodes (n)
  Boolean Formula
    Algorithm to compute winning strategy for a game of Hex. Parameterized by board size (x, y)
  Class Number
    Computational algebraic number theory; compute class group of a quadratic number field
    Parameterized by (p) number of digits after radix point for floating point numbers used
  Secure Hash Algorithm 1
    Message decrypted using SHA-1 function as oracle in Grover’s search. Parameterized by message size (n)
  Shor’s Factoring Algorithm
    Factorization using QFT. Parameterized by (n), size of bits in number to factor

## Slide 18: Results
CTQG modules are unoptimized and highly locally serialized
  ex. Shor’s algorithm has long chains of non-parallelizable rotations which require many SIMD regions to parallelize; thus k sensitive

## Slide 19: Benchmark Speedup Results
Without optimizing for communication latency, the estimated critical path runtime for Shors achieves a 10x speedup, while the actual runtimes only results in a 2-3x speedup
  Still able to achieve estimated critical path runtime
Using a communication-aware scheduler increases the runtime speedups compared to a naïve movement model
  GSE benchmark shows the largest improvement

## Slide 20: Speedup Results (continued)
Data level parallelism is able to capture most parallelism, even with relatively small k
Even though an infinite amount of data-parallelism is assumed, reducing d to 32 results in marginal changes in effectiveness
  Solely logic-level approach results in optimized architecture that can even handle additional error correction qubits

## Slide 21: Conclusion
Proposed Multi-SIMD architecture which incorporates quantum computing physical constraints works with compiler
  Ion trap technology with microwave control and quantum teleportation used as practical bases
  Scalable and maximizes parallelism while minimizing communication overhead
Hierarchical analysis scheme allows the scheduling algorithm to parallelize at coarse-grained and fine-grained levels
Produces observable speedup when evaluated against sequential execution using naïve communication model

## Slide 22: Open Problems
Level below logic level not explored
Speedup is only in comparison to naïve sequential execution
Local and global memory optimizations, latency analysis
Proposed target architecture based on theoretical assumptions for practicality

## Slide 23: Questions?